## Slide 1
External Parallel Run KPI Report
01/03/2024 – 31/05/2024
Core IDCC(a)

## Slide 2: Parallel Run KPIs
Introduction
Context
  According to Article 26(4) of the Core FB ID CCM, Core TSOs shall:
    continuously monitor the effects and the performance of the application of this methodology during the parallel run
    develop, in coordination with the Core regulatory authorities, the Agency and stakeholders, the monitoring and performance criteria and report on the outcome of this monitoring on quarterly basis in a report
  IDCC external // run started on 5th of December 2023. Since this business day, results of capacity calculation have been published on JAO website [LINK]
On the next slide the overview of the KPIs covered in this KPI report is provided.
  A Reading Guide with a detail description of the KPIs is also available on JAO [LINK]

## Slide 3: Parallel Run KPIs
Overview of parallel run KPIs
ATC related KPIs
    Duration curve of Core oriented bidding zone borders with simultaneous zero ID ATCs​
    Frequency of zero ID ATCs by oriented Core bidding zone border, and Core average​
    Frequency of isolated BZs of zero ID ATCs in import, export and both directions​
    Mean positive ID ATCs by oriented Core bidding zone border, and Core average​
    TSOs’ validation
    Monitoring of ATC based validation
    Limiting elements
    Limiting constraints of the ATC domain​

## Slide 4: Parallel Run KPIs
Reporting period and limitations
Reporting period
  This KPI report covers three months (March – May) of IDCC(a) ext//run in Core region, i.e. period 01/03/2024 – 31/05/2024.
  Due to issues in the parallel run, following results have been excluded from the KPIs:
    31/03 (rejection of some input files due to clock change),
    23/04 (no process run due to CCCt 4.0.1 deployment),
    26/04 (zero capacity provision on AT borders failed due to IT issues),
    05/05 (issues in DA process caused incorrect inputs for ID1 process).
  As a result, KPI report contains results of 88 business days.
Disclaimers
  RTE and Amprion (D7) limiting constraints at CBCO level (KPI 6) are not displayed due to limitation with input data. HR and Transnet BW (D4) might not be fully representative due to inconsistency of input data.
  ATC limiting constraints in KPI 6 are the ones which have non-negative RAM at the starting point of the ID ATC extraction and they will become limiting constraints in the end. It means there are not listed those constraints which are pre-congested constraints. However, the pre-congested constraints can also be limiting constraints with their PTDF < 0.5% in ID1.

## Slide 5: KPI 1
Duration curve of Core oriented bidding zone borders with simultaneous zero ID ATCs​

## Slide 6: KPI 2
Frequency of zero ID ATCs by oriented Core bidding zone border, and Core average​

## Slide 7: KPI 3
Frequency of isolated BZs of zero ID ATCs in import, export and both directions​​

## Slide 8: KPI 4
Mean positive ID ATCs by oriented Core bidding zone border, and Core average​

## Slide 9: KPI 5
ATC based validation

## Slide 10: KPI 6
Limiting constraints of the ATC domain​

## Slide 11: KPI 6
Limiting constraints of the ATC domain​

## Slide 12: KPI 6
Limiting constraints of the ATC domain​

## Slide 13: KPI 6
Limiting constraints of the ATC domain​

## Slide 14: KPI 6
Limiting constraints of the ATC domain​

## Slide 15: KPI 6
Limiting constraints of the ATC domain​
D2 = Tennet DE

## Slide 16: KPI 6
Limiting constraints of the ATC domain​
D4 = Transnet BW

## Slide 17: KPI 6
Limiting constraints of the ATC domain​
D8 = 50 Hertz

## Slide 18: KPI 6
Limiting constraints of the ATC domain​

## Slide 19: KPI 6
Limiting constraints of the ATC domain​

## Slide 20: KPI 6
Limiting constraints of the ATC domain​

## Slide 21: KPI 6
Limiting constraints of the ATC domain​

## Slide 22: KPI 6
Limiting constraints of the ATC domain​

## Slide 23: KPI 6
Limiting constraints of the ATC domain​

## Slide 24: KPI 6
Limiting constraints of the ATC domain​